## Slide 1: Running: How to use the eye-tracker during participant testing

## Slide 2
Host PC
Display PC
Camera
Chin Rest

## Slide 3
STEP 1: Plug in camera
1
2
STEP 2: Turn on host computer

## Slide 4
STEP 3: Adjust chin rest for participant
3
4
STEP 4: Start Matlab experiment on display computer

## Slide 5
STEP 5: Adjust camera so that eye is in view
on host computer (loosen lock knob and tilt)
6
5
STEP 6: Once in view, click on eye on host computer

## Slide 6
STEP 7: Adjust lens camera so that eye is in focus
on host computer (turn lens holder)
8
7
STEP 8: Once in focus, click Auto Threshold on host computer to set pupil and corneal threshold

## Slide 7
STEP 9: Adjust pupil and corneal threshold
9
Pupil
Corneal

## Slide 8
STEP 10: Instruct participant: “You will see a black dot
moving around on the screen. Please follow the dot
with your eyes without moving your head.”
11
STEP 11: Click Calibrate

## Slide 9
STEP 12: When they look at the first black dot (i.e., fixation point), click Accept Fixation (then let it run thru 8 points)
12

## Slide 10
STEP 13: If good, click Validate
If bad, click either Restart and go back to STEP 12 or Discard and go back to STEP 7
13

## Slide 11
STEP 14: When they look at the first black dot (i.e., fixation point), click Accept Fixation (then let it run thru 8 points)
14

## Slide 12
STEP 15: If it says GOOD, click Accept
if not, click either Restart and go back to STEP 14 or Discard and go back to STEP 7
15

## Slide 13
STEP 16: Click <ESC> on keyboard
16

## Slide 14
STEP 17: Ask participant to look at black dot and then click Accept Fixation
17